Section

61.01  Definitions

61.02  Prohibited Acts

61.03  Building Sewer Permits

61.04  Prohibited Discharges

61.05  Pretreatment of Industrial Waste

61.06  Approval of Treatment Facilities

61.07  Discharge of Unpolluted Water

61.08  Discharge of Polluted Water

61.09  Sampling of Strength of Wastewater

61.10  Unusual Flow

61.11  Comply with State and Federal Requirement

61.12  Damage to Town Sewer Works

61.13  Inspections

61.14  Violations

61.15  Fines

61.16  Violators Liable to Town of Fairmount

61.17  Difference between User and Officials

61.01  Definitions

(1)  Biochemical Oxygen Demand (BOD) means the quantity of oxygen expressed in milligram per liter, utilized in the biochemical oxidation of organic matter under standard laboratory procedures in five (5) days at twenty (20) degrees Centigrade.

(2)  Building Drain means that part of the lowest horizontal piping of a drainage system which receives the discharges from soil, waste and other drainage pipes inside the  wall of a building and conveys it to the building sewer beginning three (3) feet outside the building wall.

Building Drain - Sanitary A building drain which conveys sanitary or industrial sewage only.

Building Drain - Storm A building drain which conveys storm water or other Clearwater drainage, but no wastewater.

(3)  Building Sewer (or house connection) means the extension from the building drain to the public sewer or other place of disposal.

Building Sewer - Sanitary A building sewer which conveys sanitary or

industrial sewage only.

Building Sewer - Storm A building sewer which conveys storm water or other clearwater drainage, but no sanitary or industrial sewage.

(4)   Combined Sewer means a sewer intended to receive both wastewater and storm or surface water.

(5)  Compatible Pollutant means biochemical oxygen demand, suspended solids, PH, and fecal coliform bacterial, plus additional pollutants identified in the NPDES Permit pollutants and does remove the pollutants to a substantial degree.  The term “substantial degree” is not subject to precise definition, but generally contemplates removals in the order of eighty (80) per cent or greater.  Minor incidental removals in the order of ten (10) to thirty (30) per cent are not considered substantial.  Examples of the additional pollutants which may be considered compatible include:

A.  chemical oxygen demand,

B.  total organic carbon,

C.  phosphorus and compounds,

D.  nitrogen and nitrogen compounds, and

E.  fats, oils, and greases of animal or vegetable origin (except as prohibited where these materials would interfere with the operation of the treatment works).

(6)  Easement means an acquired legal right for the specific use of land owned by others.

(7)  Fecal Coliform  means any of a number of organisms common to the intestinal tract of man and animals, whose presence in sanitary sewage is an indicator of pollution.

(8)  Floatable Oil means oil, fat, or grease in a physical state, that will separate by gravity from wastewater by treatment in a pretreatment facility approved by the Town.

(9)  Garbage means solid wastes from the domestic and commercial preparation, cooking, and dispensing of food, and from the handling, storage and sale of produce.

(10)  Incompatible Pollutant means any pollutant that is not defined as a compatible pollutant, including non-biodegradable dissolved solids.

(11)  Industrial Waste means the liquid wastes from industrial manufacturing processes, trade, or business as distinct from sanitary sewage.

(12)  Infiltration means the water entering a sewer system, including building drains and sewers, from the ground, through means including defective pipes, pipe joints, connections, or manhole walls.  Infiltration does not include inflow.

(13)  Infiltration/Inflow means the total quantity of water from both infiltration and inflow without distinguishing the source.

(14)  Inflow means the water discharged into a sewer system, including building drains and sewers, from sources including roof leader, cellar, yard and area drains, foundation drains, unpolluted cooling water discharges, drains from springs and swampy areas, manhole covers, cross connections from storm sewers, and combined sewers, catch basins, storm waters, surface run-off, street wash waters or drainage.  Inflow does not include, and is distinguishable from, infiltration.

(15)  Inspector means the person duly authorized by the Town, through its Board of Public Works and Safety, to inspect and approve the installation of building sewers and their connection to the Town Sewer System.

(16)  Major Contributing Industry means an industry that:

A.  has a flow of at least fifty thousand (50,000) gallons or more per average work  day;

B.  has a flow greater than five percent (5%) of the flow carried by the Town system receiving the waste;

C.  has in its waste a toxic pollutant in toxic amounts as defined in standards issued under Section 307 (a) of PL 92-500; or

D.  has a significant impact, either singly or in combination with other contribution industries, on a treatment works or on the quality of effluent from the treatment works.

(17) NPDES Permit means a permit issued under the National Pollutant discharge Elimination System for discharged of wastewaters to the navigable water of the United States pursuant to Section 402, PL 92-500.

(18)  Natural Outlet  means any outlet, including storm sewers and combined sewer overflows, into a watercourse, pond, ditch, lake, or other body of surface or groundwater.

(19)  Normal  Domestic Sewage means (for the purpose of determining surcharges) wastewater or sewage having an average daily concentration as follows:

A.  (220) milligrams per liter; and

B.  Suspended solids of not more than two hundred twenty (220) milligrams per liter.

(20)  PH means the reciprocal of the logarithm of the hydrogen ion concentration.  The concentration is the weight of Hydrogen ions, in grams per liter of solution.

(21)  Person  means any user of the Town treatment works.

(22)  Pretreatment means the treatment of industrial sewage from privately owned industrial sources prior to introduction into the Town treatment works.

(23) Private Sewer means a sewer which is not owned by a public authority.

(24) Properly Shredded Garbage means the wastes from the preparation, cooking, and dispensing of food that has been shredded so that all particles will be carried freely under the flow conditions normally prevailing in public sewers, with no particle greater than one-half (1/2) inch in any dimension.

(25) Public Sewer means a sewer which is owned and controlled by the public authority and consists of the following increments:

A.  Collector Sewer means a sewer whose primary purpose is to transport wastewater from collector sewers to a treatment facility.

B.  Interceptor Sewer means a sewer whose primary purpose is to transport wastewater from collector sewers to a treatment facility.

C.  Force Main  means a pipe which wastewater is carried under pressure.

D.  Pumping Station means a station positioned in the public sewer system at which wastewater is pumped to a higher level.

(26) Sanitary Sewer means a sewer which carries sanitary and industrial wastes, and to which storm, surface, and ground water are not intentionally admitted.

(27) Sewage means the combination of the liquid and waste-carried wastes from residences, commercial building, industrial plants and institutions, (including polluted cooling water).  The three most common types of sewage are:

A. Sanitary Sewage means the combination of liquid and water-carried wastes discharged from toilet and other sanitary plumbing facilities.

B.  Industrial Sewage means a combination of liquid and water carried wastes, discharged from any industrial establishment, and resulting from any trade or process carried on in that establishment.  This includes wastes from pretreatment facilities and polluted cooling water.

C.  Combined Sewage means wastes including sanitary sewage, industrial sewage, storm water, infiltration and inflow carried to the wastewater treatment facilities by a combined sewer.

(28) Sewage Works means the structures, equipment and processes to collection, transport and treatment domestic and industrial wastes and dispose of the effluent and accumulated residual solids.

(29) Sewer  means a pipe or conduit for carrying sewage.

(30) Shall is mandatory; May is permissive.

(31)  Slug means any discharge of water or wastewater which in concentration of any given constituent or in quantity of flow exceeds for any period of duration longer than ten (10) minutes more than three (3) times the average twenty-four (24) hours concentration or flows during normal operation and will adversely affect the collection system.

(32) Standard Methods  means the laboratory procedures set forth in the latest edition, at the time of analysis, of “Standard Methods for the Examination of Water and Wastewater” prepared and published jointly by the American Public Health Association, and the American Water Works Association and the Water Pollution Control Federation.

(33)  Storm Sewer means a sewer for conveying water, ground water or unpolluted water from any source and to which sanitary and industrial wastes are not intentionally admitted.

(34) Superintendent means the Superintendent of the Town sewage works or the superintendent’s authorized deputy, agent or representative.

(35) Suspended Solids means solids that either floats on the surface of, or are in suspension in, water, sewage, or other liquids and which are removable by laboratory filtering.

(36) Total Solids means the sum of suspended an dissolved solids.

(37) Toxic Amount means concentrations of any pollutant or combination of pollutant or combination of pollutants, which upon exposure to or assimilation into any organism will cause adverse effects, such as cancer, genetic mutation, and physiological manifestations, as defined in standards issued under Section 307 (a) of PL 92-500.

(38) Unpolluted Water means water of quality equal to or better than the effluent criteria in effect, or water that would not cause violation of receiving water quality standards and would not be benefited by discharge to the sanitary sewers and wastewater treatment facilities provided.

(39) Volatile Organic Matter means the material in the sewage solids transformed to gases or vapors when heated to five hundred fifty (550) degrees Centigrade for fifteen (15) to twenty (20) minutes.

(40) Watercourse means a natural or artificial channel for the passage of water either continuously or intermittently.

61.02 Prohibited Acts

(1) A person may not place, deposit or permit to be deposited in any unsanitary manner on public or private property within the Town, or in any area under the jurisdiction of the Town, any human excrement, garbage, or other objectionable waste.

(2)  A person may not discharge or cause to be discharged to any sanitary sewer or combined sewer, either directly or indirectly, stormwater, surface water, ground water, roof runoff, subsurface drainage, cooling water, unpolluted water, or unpolluted industrial process water.  The Town shall require the removal of unpolluted wastewater collection or treatment facility if that removal is cost-effective and in the best interests of all users of those facilities.

(3)  Stormwater, surface water, ground water, roof runoff, sub-surface drainage, cooling water, unpolluted water or unpolluted industrial process water may be admitted to storm sewer which have adequate capacity for their accommodation.  A person may not use these sewers, however, without the specific permission of the town.

(4)  No new connection shall be made unless there is capacity available to all downstream sewers, lift stations, force mains, and the sewage treatment plant, including capacity for BOD and suspended solids.

(5)  A person may not place, deposit or permit to be deposited any  unsanitary manner on public or private property within the jurisdiction of the Town, any wastewater or other polluted waters except where suitable treatment has been provided in accordance with provisions of this Code section and the NPDES Permit.

(6)  A person may not discharge or cause to be discharged to any natural outlet any wastewater or other polluted waters except where suitable treatment has been provided in accordance with provisions of this Code section and the NPDES Permit.

(7)  Except as provided in this Code section, no person may construct or maintain any privy, privy vault, septic tank, cesspool, or other facility intended or used for the disposal of sewage.

(8)  The owner of a house, building or property used for human occupancy, employment, recreation or other purposes, situated within the Town and abutting on any street, alley, or right-of-way in which there is located on May 9, 1983, a Town public sanitary or combined sewer shall, at the owner’s expense, install suitable toilet facilities in that structure, and connect the facilities directly with the proper public sewer in accordance with the provisions of this Code section, within ninety (90) days after date of official notice to do so, if the public sewer is within one hundred (100) feet of the property line.

61.03 Building Sewer Permit

(1)  An unauthorized person may not uncover, make any connection with or opening into, use, alter, or disturb any public sewer or appurtenance of it without first obtaining a written permit from the Clerk-Treasurer.

(2)  There shall be two (2) classes of building sewer permits:

A.  For residential and commercial service; and

B.  For service to establishments producing industrial wastes.

In either case, the owner or the owner’s agent shall make application of the form furnished by the Town.  The permit application must be supplemented by any plans, specifications, or other information considered pertinent in the judgment of the Inspector.  A permit and inspection fee of Three Hundred Dollars ($300) for a residential with the Utility supplying a stainless steel saddle for the tap.  The Town Council shall determine all commercial and industrial building sewer permits fees.  All permit fees shall be paid to the Clerk-Treasurer when application is filled.

(3)  All costs and expense incident to the installation and connection of the building sewer shall be borne by the owner.  The owner shall indemnify the Town form any loss or damage that may directly or indirect5ly be occasioned by the installation of the building sewer.

(4)  A separate and independent building sewer shall be provided for every building.  This requirement does not apply where one (1) building stands at the rear of another on an interior lot and no private sewer is available or can be constructed to the rear building through an adjoining alley, courtyard, or driveway.  In that case, the building sewer from the front building may be extended to the rear building and the whole considered as one building sewer.

(5)  Building sewers already existing on the property may be used in connection with new buildings if they are found, on examination and test by the Inspector, to meet all requirements of this Code section.

(6)  The size, slope alignment, materials of construction of a building sewer, and the methods to be used in excavating, placing of the pipe, jointly testing, and backfilling the trench, shall conform to the requirements of the Town building and plumbing code or other applicable Town rules and regulations.  In the absence of code provisions or the amplify them, the materials and procedures set forth in appropriate specification of the A.S.T.M. and W.P.C.F. manual of Practice No 98 shall apply.

(7)  Whenever possible, the building sewer shall be brought to the building at an elevation below the basement floor. In all buildings where the drain is too low to permit gravity flow to the public sewer, sanitary sewage carried by the building drain must be lifted by an approved means and discharged to the building sewer.

(8)  A person may not make connection of roof downspouts, exterior foundation drains, areaway drains, or other source of surface run-off or groundwater to a building sewer or building drain which in turn is connected directly or indirectly to a public sanitary sewer.

(9)  The connection of the building sewer into the public sewer shall conform to the requirements of the Town Building and plumbing code or other applicable Town rules and regulations, or the procedures set forth in appropriate specifications of the A.S.T.M. and the W.P.C.F. Manual of Practice No. 9.  All connections must be made gas tight and watertight.  Any deviation from the prescribed procedures and materials must be approved by the Superintendent  before installation.

(10) the applicant for the building sewer permit shall notify the Inspector when the building sewer is ready for inspection and connection to the public sewer.  The connection must be made under the supervision of the Inspector or his representative.

(11) All excavations for building sewer installation must be adequately guarded with barricades and lights to protect the public from hazard.  Streets, sidewalks parkways, and other public property disturbed in the course of the work must be restored in a manner satisfactory to the Town.

61.04  Prohibited Discharges

(1) A person may not discharge or cause to be discharged any of the following described waters or wastes to any public sewers:

A.  Any gasoline, benzene, naphtha, fuel oil or other flammable or explosive liquid, solid or gas.

B.  Any water or wastes containing toxic or poisonous solids, liquids, or gases in sufficient quantity, either singly or by interaction with other wastes, to injure or interfere with any sewage treatment process, constitute a hazard to humans or animals, create a public nuisance, or create any hazard in the receiving waters of the sewage treatment plant.

C.  Any waters or wastes having a PH lower than 5.5, and having any oth4er corrosive property capable of causing damage or hazard to structure, equipment, and personnel of the sewage works, or that interferes with any treatment process.

D.  solid or viscous substances in quantities or of a size capable of causing obstruction to the flow is sewers, or their interference with the proper operation of the sewage works including ashes, cinders, sand, mud, straw, shavings, metal, glass, rages, feathers, tar, plastics, wood, unground garbage, whole blood, paunch, manure, hair and fleshing, entrails, paper, dishes, cups, milk containers, etc., either whole or ground by garbage grinders.

(2)  A person may not discharge or cause to be discharged the following substances, materials or wastes if it appears likely, in the opinion of the Superintendent that the wastes could harm either the sewers, sewage treatment process, or equipment, have a adverse effect on the receiving stream, or can otherwise endanger life, limb, public property, or constitute a nuisance.  In forming an opinion concerning the acceptability of these wastes, the Superintendent will give consideration to factors including the quantities of subject wastes in relation to flows and velocities in the sewers, materials of construction of the sewers, nature of the sewage treatment process, capacity of the sewage treatment plant, and other pertinent factors. The substances prohibited are:

A.  Any liquid or vapor having a temperature higher than one hundred fifty (150) degrees Fahrenheit or sixty-five (65) degrees Centigrade.

B.  Any water or waste containing fats, wax, grease, or oil, whether emulsified or not, in excess of one hundred (100) milligrams per liter or containing substances which may solidify or become viscous at  temperatures between thirty-two (32) and one hundred fifty (150) degrees Fahrenheit or zero and  sixty-five (0 and 65) degrees Centigrade.

C.  Any garbage that has not been properly shredded.  The installation and operation of any garbage grinder equipped with a motor of three-fourths (3/4) horsepower (0.76 HP metric) or greater must be reviewed and approved by the Superintendent.

D.  Any waters or wastes containing strong acid iron pickling wastes, or concentrated plating solutions whether neutralized or not.

E.   Any waters or wastes containing iron, chromium, copper, zinc, and similar objectionable or toxic substances; or wastes exerting an excessive chlorine requirement, to the degree that any such material received in the composite sewage at the sewage treatment works exceeds the limits established by the Superintendent for such materials.

F.  any waters or wastes containing phenols or other taste or odor producing substances, in concentrations exceeding limits which may be established by the Superintendent as necessary, after treatment of the composite sewage, to meet the requirement of the State, Federal or other public agencies of jurisdictions of such discharge to the receiving waters.

G.  any radioactive wastes or isotopes with a half life or concentration exceeding limits established by the Superintendent in compliance with applicable State or Federal Regulations.

H.  Any waters or wastes having a PH in excess of 9.5.

I.  Materials which exert a cause:

(i)  Unusual concentrations of inert suspended solids including fullers earth, lime slurries, and lime residues, or of dissolved solids including sodium chloride and sodium sulfate.

(ii)  Excessive discoloration including dye wastes and vegetable tanning solutions.

(iii)  Unusual BOD, chemical oxygen demand, or chlorine requirements in quantities which constitute a significant load on the sewage treatment works.

(iv)  Unusual volume of flow of concentration of wastes constituting “slugs”.

J.  Waters and wastes containing substances which are not amendable to treatment or reduction by the sewage treatment processes employed, or are amendable to treatment only to the degree that the sewage treatment effluent cannot meet the requirements of other agencies having jurisdiction over discharge to the receiving waters.

3.  If any waters or wastes are discharged, or are proposed to be discharged, to the public sewers, which waters contain the substances or possess the characteristics enumerated in subsection (e) (2) of this Codes section, and which in the judgment of the Superintendent may have a deleterious effect upon the sewage works, processes, equipment, or receiving waters, or which otherwise create a hazard to life or constitute a public nuisance, the Superintendent may:

a.  Require new industries or industries with significant increase in discharges to submit information on wastewater characteristics and obtain prior approval for discharges.

b.  Reject the wastes in whole or part for any reason deemed appropriate by the Town.

c.  Require pretreatment of wastes to within the limits of normal sewage as defined in this Code section.

d.  Require control or flow equalization of the wastes so as to avoid any “slug” load or excessive loads that may be harmful to the treatment works, or

e.  Require payment of a surcharge or any excessive flows or loadings discharged to the treatment works to cover the additional cost of having capacity for the treating these wastes.

If the Superintendent permits the pretreatment or equalization of waste flows,  the design and installation of the plant and equipment shall be reviewed and approved by the Superintendent and subject to all requirements imposed by applicable codes, ordinances and laws.

4.  Where preliminary treatment of flow-equalizing facilities are provided for any waters and wastes, they shall be maintained continuously in satisfactory and effective operation by the owner at the owner’s expense.

5.  When required by the Superintendent, the owner of any property serviced by a building sewer carrying industrial wastes shall install a suitable control manhole together with the necessary meters and other appurtenances in the building sewer to facilitate observation, sampling, and measurement of the wastes.  The manhole, when required, must be accessibly and safely located, and be constructed in accordance with plans approved by the Superintendent.  The manhole shall be maintained by the owner to be safe and accessible at all times.  Agents of the Town, the State Water Pollution Control Agencies, and the U. S. environmental Protection Agency may enter all properties to inspect, observe, measure, sample and test.

6.  All measurements, tests, and analyses of the characteristics of water and wastes to which reference is made in this Code section shall be determined in accordance with the latest edition of “Standard Methods for the Examination of Water and Wastewater”, published by the American Public Health Association, and shall be determined at the control manhole provided, or upon suitable samples taken at the control manhole, except for application of NPDES permits and the report of it which shall be conducted in accordance with rules and regulations adopted by the USEPA published in the Federal Register on October 16, 1973, (38 CFR 20758) and any subsequent revisions subject to approval by the Town.  If no special manhole has been required, the control manhole shall be considered to be the nearest downstream manhole in the public sewer to the point at which the building sewer is connected.   Sampling shall be carried out by customarily accepted methods to reflect the effect of constituents upon the sewage works and to determine the existence of hazards  to life, limb, and property.  The particular analysis involved will determine whether a twenty-four (24) hour composite of all outfalls of a premises is appropriate or whether a grab sample or sample should be taken.  Normally, but not always, BOD suspended solids analysis will be obtained from twenty-four (24) hours composites of all outfalls, whereas PH’s will be determined from periodic grab sample.

7.  No statement in this Code section shall be construed as preventing any agreement or arrangement between the Town and any industrial concern under which an industrial waste of usual strength or character may be accepted by the Town for treatment, subject to payment by the industrial concern at rates compatible with Town Code section Chapter 60.

61.05 Pretreatment of Industrial Wastes

Pretreatment of industrial wastes from major contribution industries prior to discharge to the treatment works is required and is subject to the rules and regulations adopted by the United States Environmental Protection Agency (USEPS) and published in the Federal Register on August 25, 1978, (43 CFR part 23), and “Federal Guidelines Establishing Test procedures for Analysis of Pollutants” published in the Federal Register on October 16, 1973, (40 CRR part 136,) in addition to any more stringent requ8irements established by Town, and any subsequent State and Federal guidelines, rules and regulations.

61.06 Approval from Town for Treatment Facilities

Plans, specifications and any other pertinent information relating to pretreatment or control facilities shall be submitted to the approval of the Town.  No construction of facilities may be commenced until the Town Grants approval in writing.  Where these facilities are provided, they shall be maintained continuously in satisfactory and effective operating order by the owner at the owner’s expense and shall be subject to periodic inspection by the Town to determine that the facilities are being operated in conformance with the applicable Federal, State and Town Laws, ordinances, and permits.  The owner shall maintain operating records of the influent and effluent to show the performance of the treatment facilities and for comparison against Town monitoring records.

61.07  Discharge of Unpolluted Water

Unpolluted water from air conditioners, cooling, condensing systems, or swimming pools shall be discharged to a storm sewer, where available, or to a combined sewer discharged may be to a natural outlet approved by the Town and by the State.  If a storm sewer, combined sewer, or natural sewer is not available, unpolluted water may be discharged to a sanitary sewer pending written approval by the Town.

61.08  Discharge of Polluted Water

(1)  Industrial cooling water, which may be polluted with insoluble oils or grease or suspended solids, shall be pretreated for removal of pollutants.  The resultant clear water shall be discharged in accordance with the above section.

(2)  The Town may require users of the treatment works, other than residential users, to supply pertinent information on wastewater flows characteristics.  The measurements, tests, and analyses shall be made at the users’ expense.  If made by the Town, the Town may assess an appropriate charge.

61.09  Sampling of Strength of Wastewaters

The strength of wastewaters shall be determined, for periodic establishment of charges provided for in Town Code Section Chapter 60, from samplings taken at the structures mentioned in this Code section at any period of time and of the duration and manner elected by the Town, or, at any place mutually agreed upon between the user and the Town.  The Town may asses appropriate charges for sampling and analysis.  The results of routing sampling and analysis by the user may also be used for determination of charges after verification by the Town.

61.10  Grease, Oil & Sand Interceptors or Traps Required

Grease, oil and sand interceptors or traps shall be provided when, in the opinion of the Town, they are necessary for the proper handling of liquid wastes containing grease in excessive amounts, or any flammable wastes, and other harmful ingredients, except that the interceptors or traps will not be required for private living quarters or dwelling units.  All interceptors or traps must be of a type and capacity approved by the Town and located to be readily accessible for cleaning and inspection.  They must be constructed of impervious materials capable of withstanding abrupt and extreme changes in temperatures and of  substantial construction, gas tight, water tight, and equipped with easily removable covers.  Where installed, all grease, oil and sand interceptors or traps must be maintained by the owner, at the owner’s expense, in continuously efficient operation at all times.

61.11  Unusual Flows or Wastes

Users of the treatment works shall immediately notify the Town of any unusual flows or wastes that are discharged into the sewer system.

61.12  Code must comply with State and Federal

All provisions of this Code section and the limits set in it must comply with any applicable State and Federal requirements in effect on or after May 9, 1983.

61.13  Damage Town Sewer Works

An unauthorized person may not maliciously, willfully or negligently break, damage, uncover, deface, or tamper with any structure appurtenance, or equipment which is a part of the Town sewage works.

61.14  Inspections

1.  The Superintendent, Inspector and any other duly authorized Town Employee bearing proper credentials and identification may enter all properties to inspect, observe, measure, sample, and test in accordance with this Code section.  The Superintendent or the Superintendent’s representative may not inquire into any process including metallurgical, chemical, oil, refining, ceramic, paper, or other industries beyond that point have a direct bearing on the kind and source of discharge to the sewers or water ways or facilities for waste treatment.

2.  While performing the necessary works on private properties referred to in subsection (61.11) (1), the Superintendent or the duly authorized Town employee shall observe all safety rules applicable to the premises established by the company.  The company shall be held harmless for injury or death to the Town employees and the Town shall indemnify the company against liability claims and demands for personal injury or property damage asserted against the company and growing out of the gauging and sampling operation, except those caused by negligence or failure of the company to maintain safe conditions as required in Section (61.04) (5).

3.  The superintendent and other duly authorized Town employees bearing proper credentials and identification may enter all private properties through which the Town holds a duly negotiated easement to inspect, observe, measure, sample repair, and maintain any portion of the sewage works lying within the easement.  All entry and subsequent work, if any, on the easement, must be done in full accordance with the terms of the duly negotiated easement pertaining to the private property involved.

61.15  Violations

Any person who violates any provision of this Code section except subsection (61.12) (3) shall be served by the Town with written notice stating the nature of the violation and providing a reasonable time limit for its satisfactory correction.  The offender shall, within the period of time stated in the notice, permanently cease all violations.

61.16  Fines

Any person who continues any violation beyond the time limit provided for in Section (61.14) commits an ordinance violation and upon on conviction, shall be fined not more than five hundred dollars ($500) for each violation.  Each day a violation continues constitutes a separate ordinance violation.

61.17  Violators Liable to the Town

Any person violating any provisions of this Code section is liable to the Town for any expense, loss, or damage occasioned by the Town by reason of the violation.

61.18  Difference Between Users and Officials

Any difference that arises between users and officials of the Town Sewage Works that cannot be resolved at the level may be appealed to the Board.

Ordinance 9-1983, adopted May 9, 1983

Ordinance 7-2002, adopted July 22, 2002